## Slide 1: اكاسيد النتروجين

## Slide 2: انواع اكاسيد النتروجين
بالاضافة الى النتروجين الجوي تتضمن
غاز اوكسيد النتروز (غاز الضحك) N2O
اول اوكسيد النتريك NO
ثنائي اوكسيد النتروجين NO2
الامونيا NH3
يحتاج تكون اكاسيد النتروجين (NO& NO2) الى درجات حرارة عالية تصل الى 1100 درجة مؤية

## Slide 3: مصادر مركبات النتروجين
الامونيا ينبعث سنويا 868 مليون طن من العمليات البايلوجية
غاز اوكسيد النتروز ينبعث سنويا 343 مليون طن من العمليات البايلوجية
اوكسيد النتريك ينبعث سنويا 212 مليون طن سنويا من العمليات البايلوجية وكذلك ينتج من مصادر بشرية
ثنائي اوكسيد النتروجين ينبعث سنويا 14.6 مليون طن سنويا من عمليات الاحتراق

## Slide 4: مسارات تواجدها
الامونيا تترسب الى الارض او المياه كونها ذائبة في الماء
اوكسيد النتروز اكثر استقرارية من بقية مركبات النتروجين ولذا يوجد بتراكيز عالية في التروبوسفير
اما مسار اول اوكسيد النتريك وثنائي اوكسيد النتروجين فيكون اكثر تعقيدا

## Slide 5
يتأكسد NO بواسطة الاوكسجين او الاوزون على فترة تمتد من 2-6 ايام
NO +O +M →NO2 +M
NO + O3 → NO2 + O2

## Slide 6
يبقى جزيء NO2 في الجو 3 ايام فقط في المتوسط
وتتم عملية ازالته كالتاي
NO2 + H2O ↔HNO3 + HNO2

## Slide 7: اثار مركبات النتروجين
يعرف عن اكاسيد النتروجين انها تسبب بهتان الوان اصباغ النسيج وتلف القطن والنايلون وتاكل الفلزات
تتاثر بعض النباتات الحساسة بشكل كبير من تراكيز للNO2 تبلغ جزء واحد بالمليون لمدة يوم واحد (تلف الوراق وانخفاض معد النمو) او بكمية قليلة تساوي 0.25 جزء بالمليون لبضعة اشهر
للاوكسجين الفة غير طبيعية للNO نحو 1500 مرة اكثر من الفته للCO الا انه من حسن الحظ غير قادر على الدخول الى مجرى الدم ليتفاعل مع الهيموكلوبين
NO2 غاز ضارب للحمرة يمكن الاحساس برائحته بتركيز 0.12 جزء بالمليون
ان تركيز 100 جزء بالمليون لبضعة دقائق تؤدي الى تاثيرات ضارة على الجهاز التنفسي
والتعرض الى 15-50 جزء بالمليون لمدة ساعتين يؤدي الى تلف الرئتين والقلب والكبد والكليتين

## Slide 8
At room temperature, Nitric Oxide is a colorless, nonflammable, poisonous, oxidizing gas with an irritating odor. Nitric Oxide is extremely toxic by inhalation, and symptoms of over-exposure may not become apparent for up to 72 hours. The gas is an oxidizer and will support and enhance combustion. Emergency responders must protect themselves from inhalation. A water spray can be used to control and direct a release. In the presence of air, Nitric Oxide forms brown fumes of nitrogen dioxide and is extremely reactive and a strong oxidizing agent. Emergency responders must wear the proper personal protective equipment suitable for the situation to which they are responding.

## Slide 9
INHALATION: Exposure to Nitric Oxide gas in low concentrations produces an irritating effect on the mucous membranes of the eyes, nose, throat and lungs, which can include choking, coughing, headache, nausea and fatigue. Severe over-exposure may cause methemoglobinemia, cyanosis, delayed pulmonary edema, mental confusion, unconsciousness and death. High concentrations of Nitric Oxide gas may cause an oxygen-deficient atmosphere; however, other more significant health effects will occur prior to those for oxygen deficiency. Nitric Oxide can react in the body to oxidize hemoglobin to methemoglobin in the blood. Coma and death can ensue when methemoglobin levels reach 70%. The inability of methemoglobin to

## Slide 10
combine with oxygen can result in clinical effects due to tissue hypoxia. Symptoms include muscular tremors, drowsiness, a brownish-blue hue to the mucous membranes, increased heart rate, vertigo and vomiting

## Slide 11
INHALATION:
The Nitrogen Dioxide component of this gas mixture
is toxic. Inhalation over-exposures to this
gas mixture may result in severe irritation and bur
ns of eyes, skin, mucous membranes, and any other
exposed tissue. Delayed pulmonary damage and breathing di
fficulty may also occur. Severe inhalation
over-exposures can be fatal. All of the symp
toms described above may be aggravated by physical
exertion. Based on animal information an increased sens
itivity to allergens and bacterial infections may
occur as a result of inhalati
on exposure to Nitrogen Dioxide.
As a result of severe over-exposures to this gas
mixture, permanent lung injury may occur. Prolonged or
repeated over-exposures to this gas mixture may
cause impaired lung function, bronchitis, hacking
cough, nasal irritation and discharge, increased fatigue,
decreased immune response and dental erosion.
Note: symptoms can develop after over-exposure to
concentrations of Nitrogen Dioxide in ranges which
exist in this gas mixture. The onset of the sy
mptoms of pulmonary edema can be delayed for hours or
days after the exposure.

## Slide 12
HEALTH EFFECTS OR RISKS FROM EXPOSURE:
Over-exposure to this gas mixture may cause the
following health effects:
ACUTE:
Over-exposures may result in severe irrita
tion and burns of eyes, skin, mucous membranes, and
any other exposed tissue. If high c
oncentrations of this gas mixture are inhaled, delayed pulmonary damage
and breathing difficulty may occur. Severe inhalation
over-exposures can be fatal, as a result of lung
damage.
CHRONIC:
Prolonged or repeated over-exposures to this
gas mixture may cause impaired lung function,
bronchitis, coughing, nasal irritation and discharge,
increased fatigue, decreased immune system response,
and dental erosion. Refer to Section 11 (T
oxicology Information) for additional data.
TARGET ORGANS:
ACUTE: Respiratory system, skin, eyes
. CHRONIC: Skin, respiratory system, immune
system.
HMIS RATIN

## Slide 13: With my thank