## Slide 1: Process Engineering
Dr . nadia al waely
Notes: <number>

## Slide 2: Chapter 6. PROCESS ENGINEERING
• Process planning is also called: manufacturing planning, process planning, material processing, process engineering, and machine routing.
• Which machining processes and parameters are to be used (as well as those machines capable of performing these processes) to convert (machine) a piece part from its initial form to a final form predetermined (usually by a design engineer) from an engineering drawing.
• The act of preparing detailed work instructions to produce a part.
• How to realize a given product design.
Notes: <number>

## Slide 3: PRODUCT REALIZATION
Product design
Process planning
Operation programming
Verification
Scheduling
Execution
Process,
machine
knowledge
Scheduling
knowledge
Notes: <number>

## Slide 4: PROCESS PLANNING
Design
Machine
Tool
Scheduling and Production Control
Process
Planning
Notes: <number>

## Slide 5: PROBLEMS FACING MANUFACTURING INDUSTRY
Fact:
  Only 11% of the machine tools in the U.S. are programmable.
  More than 53% of the metal-working plants in the U.S. do not have even one computer-controlled machine.
Some problems:
  Cannot justify the cost
  Lack of expertise in using such machines
  Too small a batch size to offset the planning and programming costs
Source: Kelley, M.R. and Brooks, H., The State of Computerized Automation in US Manufacturing, J.F. Kennedy School of Government, Harvard University, October 1988.
  Potential benefits in reducing turnaround time by using programmable machine tools have not been realized due to time, complexity and costs of planning and programming.
Notes: <number>

## Slide 6: DOMAIN
One-of-a-kind and Small batch
Objectives: Lead-time, Cost
Approaches: process selection, use
existing facilities.
Mass production
Objective: Cost
Approaches: process design, optimization,
materials selection, facilities
design
Notes: <number>

## Slide 7: How do we process engineer?
How can we make it?
How much does it cost?
How long will it take us to complete it?
How reliable will it be?
How can we recycle it
Notes: <number>

## Slide 8: How can we make it?
Is this like something else that we’ve done?
  Yes; What methods were used?
  No; Design a new process
Notes: <number>

## Slide 9: What methods were used?
Machining methods
Pressworking
Welding/fabrication
Casting
Powder materials
Layered deposition
Others
Notes: <number>

## Slide 10: Welding/fabrication: Additive techniques
+
+
=
Initial
Stock
Weld
Add-on
Weld
Add-on
Final Product
Notes: <number>

## Slide 11: Machining Methods: Subtractive techniques
-
=
Initial
Stock
Slotting
Drilling
Final Product
-
=
Notes: <number>

## Slide 12: Casting: Form Methods
=
Notes: <number>

## Slide 13: ENGINEERING DESIGN MODELING
CSG MODEL
B-REP MODEL
Notes: <number>

## Slide 14: INTERACTION OF PLANNING FUNCTIONS
GEOMETRIC REASONING
PROCESS SELECTION
CUTTER SELECTION
MACHINE TOOL SELECTION
SETUP PLANNING
FIXTURE PLANNING
CUTTER PATH GENERATION
• global & local geometry
• process capability
• process cost
• available tools
• tool dimension and geometry
• geometric constraints
• machine availability, cost
• machine capability
• feature relationship
• approach directions
• process constraints
• fixture constraints
• fixture element function
• locating, supporting, and
clamping surfaces
• stability
• feature merging and split
• path optimization
• obstacle and interference
avoidance
Notes: <number>

## Slide 15: PROCESS PLAN
• Also called : operation sheet, route sheet, operation planning summary, or another similar name.
• The detailed plan contains:
route
processes
process parameters
machine and tool selections
fixtures
• How detail the plan is depends on the application.
• Operation: a process
• Operation Plan (Op-plan): contains the description of an operation, includes tools, machines to be used, process parameters, machining time, etc.
• Op-plan sequence: Summary of a process plan.
Notes: <number>

## Slide 16: EXAMPLE PROCESS PLANS
Detailed Process Plan
Oper. Routing Summary
Notes: <number>

## Slide 17: FACTORS AFFECTING PROCESS PLAN SELECTION
• Shape
• Tolerance
• Surface finish
• Size
• Material type
• Quantity
• Value of the product
• Urgency
• Manufacturing system itself
• etc.
Notes: <number>

## Slide 18: PROCESS PLANNING CLASSIFICATION
MANUAL
COMPUTER-AIDED
VARIANT
GT based
Computer aids for editing
Parameters selection
GENERATIVE
Some kind of decision logic
Decision tree/table
Artificial Intelligence
Objective-Oriented
Still experience based
AUTOMATIC
Design understanding
Geometric reasoning capability
Notes: <number>

## Slide 19: REQUIREMENTS IN MANUAL PROCESS PLANNING
• ability to interpret an engineering drawing.
• familiar with manufacturing processes and practice.
• familiar with tooling and fixtures.
• know what resources are available in the shop.
• know how to use reference books, such as machinability data handbook.
• able to do computations on machining time and cost.
• familiar with the raw materials.
• know the relative costs of processes, tooling, and raw materials.
Notes: <number>

## Slide 20: INDUSTRIAL SOLUTION
PRODUCT
CONCEPT
CAD
CAM
CUTTER
PATH
HUMAN - decision making
COMPUTER - geometric computation, data handling
N0010 G70 G 90 T08 M06
N0020 G00 X2.125 Y-0.475 Z4.000 S3157
N0030 G01 Z1.500 F63 M03
N0040 G01 Y4.100
N0050 G01 X2.625
N0060 G01 Y1.375
N0070 G01 X3.000
N0080 G03 Y2.625 I3.000 J2.000
N0090 G01 Y2.000
N0100 G01 X2.625
N0110 G01 Y-0.100
N0120 G00 Z4.000 T02 M05
N0130 F9.16 S509 M06
N0140 G81 X0.750 Y1.000 Z-0.1 R2.100 M03
N0150 G81 X0.750 Y3.000 Z-0.1 R2.100
N0160 G00 X-1.000 Y-1.000 M30
Notes: <number>

## Slide 21: PROCESS PLANNING STEPS
Study the overall shape of the part. Use this information to classify the part and determine the type of workstation needed.
• Thoroughly study the drawing. Try to identify every manufacturing features and notes.
If raw stock is not given, determine the best raw material shape to use.
Identify datum surfaces. Use information on datum surfaces to determine the setups.
• Select machines for each setup.
For each setup determine the rough sequence of operations necessary to create all the features.
Notes: <number>

## Slide 22: PROCESS PLANNING STEPS (continue)
Sequence the operations determined in the previous step.
Select tools for each operation. Try to use the same tool for several operations if it is possible. Keep in mind the trade off on tool change time and estimated machining time.
Select or design fixtures for each setup.
Evaluate the plan generate thus far and make necessary modifications.
Select cutting parameters for each operation.
Prepare the final process plan document.
Notes: <number>

## Slide 23: COMPUTER-AIDED PROCESS PLANNING
ADVANTAGES
1. It can reduce the skill required of a planner.
2. It can reduce the process planning time.
3. It can reduce both process planning and manufacturing cost.
4. It can create more consistent plans.
5. It can produce more accurate plans.
6. It can increase productivity.
Notes: <number>

## Slide 24: WHY AUTOMATED PROCESS PLANNING
• Shortening the lead-time
• Manufacturability feedback
• Lowering the production cost
• Consistent process plans
Notes: <number>

## Slide 25: PROCESS PLANNING
Machining features
Design
Workpiece Selection
Process Selection
Tool Selection
Feed, Speed Selection
Operation Sequencing
Setup Planning
Fixturing Planning
Part Programming
Notes: <number>

## Slide 26: VARIANT PROCESS PLANNING
GROUP TECHNOLOGY BASED RETRIEVAL SYSTEM
Notes: <number>

## Slide 27: PROBLEMS ASSOCIATED WITH THE VARIANT APPROACH
1. The components to be planned are limited to similar components previously planned.
2. Experienced process planners are still required to modify the standard plan for the specific component.
3. Details of the plan cannot be generated.
4. Variant planning cannot be used in an entirely automated manufacturing system, without additional process planning.
Notes: <number>

## Slide 28: ADVANTAGES OF THE VARIANT APPROACH
1. Once a standard plan has been written, a variety of components can be planned.
2. Comparatively simple programming and installation (compared with generative systems) is required to implement a planning system.
3. The system is understandable, and the planner has control of the final plan.
4. It is easy to learn, and easy to use.
Notes: <number>

## Slide 29: GENERATIVE APPROACH
A system which automatically synthesizes a process plan for a new component.
(i) part description
(ii) manufacturing databases
(iii) decision making logic and algorithms
MAJOR COMPONENTS:
Notes: <number>

## Slide 30: ADVANTAGES OF THE GENERATIVE APPROACH
1. Generate consistent process plans rapidly;
2. New components can be planned as easily as existing components;
3. It has potential for integrating with an automated manufacturing facility to provide detailed control information.
Notes: <number>

## Slide 31: KEY DEVELOPMENTS
1. The logic of process planning must be identified and captured.
2. The part to be produced must be clearly and precisely defined in a computer-compatible format
3. The captured logic of process planning and the part description
Notes: <number>

## Slide 32: PRODUCT REPRESENTATION
Geometrical information
Part shape
Design features
Technological information
Tolerances
Surface quality (surface finish, surface integrity)
Special manufacturing notes
Etc.
"Feature information"
Manufacturing features
e.g. slots, holes, pockets, etc.
Notes: <number>

## Slide 33: INPUT REPRESENTATION SELECTION
• How much information is needed?
• Data format required.
• Ease of use for the planning.
• Interface with other functions, such as, part programming, design, etc.
• Easy recognition of manufacturing features.
• Easy extraction of planning information from the representation.
Notes: <number>

## Slide 34: WHAT INPUT REPRESENTATIONS
GT CODE
Line drawing
Special language
Symbolic representation
Solid model
CSG
B-Rep
others?
Feature based model
Notes: <number>

## Slide 35: SPECIAL LANGUAGE
AUTAP
Notes: <number>

## Slide 36: CIMS/PRO REPRESENTATION
Notes: <number>

## Slide 37: GARI REPRESENTATION
(F1 (type face) (direction xp) (quality 120))
(F2 (type face) (direction yp) (quality 64))
(F3 (type face) (direction ym) (quality rough))
(H1 (type countersunk-hole) (diameter 1.0)
(countersik-diameter 3.0)
(starting-from F2) (opening-into F3))
(distance H1 F1 3.0)
(countersink-depth F2 H1 0.5)
Notes: <number>

## Slide 38: CONCEPT OF FEATURE
Manufacturing is "feature" based.
Feature:
1 a: the structure, form, or appearance esp. of a person
b: obs: physical beauty.
2 a: the makeup or appearance of the face or its parts
b: a part of the face: LINEAMENT
3: a prominent part or characteristic
4: a special attraction
Webster's Ninth New Collegiate Dictionary
Notes: <number>

## Slide 39: FEATURES IN DESIGN AND MANUFACTURING
A high level geometry which includes a set of connected geometries. Its meaning is dependent upon the application domain.
Design Feature vs Manufacturing Feature
Notes: <number>

## Slide 40: DESIGN FEATURES
• For creating a shape
• For providing a function
Slot feature
Notes: <number>

## Slide 41: MANUFACTURING FEATURES
• For process selection
• For fixturing
End mill a slot
Drilling Round hole
Turning Rotational feature
End milling Plane surface,
Hole, profile, slot
pocket
Ball end mill Free form surface
Boring Cylindrical shell
Reaming Cylindrical shell
... ...
Manufacturing
is feature based.
Notes: <number>

## Slide 42: MANUFACTURING FEATURES (cont.)
?
Notes: <number>

## Slide 43: DATA ASSOCIATED WITH DESIGN FEATURES
Mechanical Engineering Part Design
• Feature Type
• Dimension
• Location
• Tolerance
• Surface finish
• Function
Notes: <number>

## Slide 44: DATA ASSOCIATED WITH MANUFACTURING FEATURES
• Feature type
• Dimension
• Location
• Tolerance
• Surface finish
• Relations with other features
• Approach directions
° Feature classifications are not the same.
Notes: <number>

## Slide 45: FEATURE RECOGNITION
Extract and decompose features from a geometric model.
• Syntactic pattern recognition
• State transition diagram and automata
• Decomposition
• Logic
• Graph matching
• Face growing
Notes: <number>

## Slide 46: DIFFICULTIES OF FEATURE RECOGNITION
• Potentially large number of features.
• Features are domain and user specific.
• Lack of a theory in features.
• Input geometric model specific. Based on incomplete models.
• Computational complexity of the algorithms.
• Existing algorithms are limited to simple features.
Notes: <number>

## Slide 47: DESIGN WITH MANUFACTURING FEATURES
Make the design process a simulation of the manufacturing process. Features are tool swept volumes and operators are manufacturing processes.
Design
Process Planning
Bar stock - Profile - Bore hole
Turn profile
Drill hole
Bore hole
Notes: <number>

## Slide 48: PROS AND CONS OF DESIGN WITH MANUFACTURING FEATURES
• Concurrent engineering - designers are forced to think about manufacturing process.
• Simplify (eliminate) process planning.
• Hinder the creative thinking of designers.
• Use the wrong talent (designer doing process planning).
• Interaction of features affects processes.
Pros
Cons
Notes: <number>

## Slide 49: BACKWARD PLANNING
Notes: <number>

## Slide 50: PROCESS KNOWLEDGE REPRESENTATION
• Predicate logic
• Production rules
• Semantic Nets
• Frames
• Object Oriented Programming
Notes: <number>

## Slide 51: SOME RESEARCH ISSUES
• Part design representation: information contents, data format
• Geometric reasoning: feature recognition, feature extraction, tool approach directions, feature relations
• Process selection: backward planning, tolerance analysis, geometric capability, process knowledge, process mechanics
• Tool selection: size, length, cut length, shank length, holder, materials, geometry, roughing, and finishing tools
Notes: <number>

## Slide 52: SOME RESEARCH ISSUES (continue)
• Fixture design: fixture element model, fixturing knowledge modeling, stability analysis, friction/cutting force
• Tool path planning: algorithms for features, gauging and interference avoidance algorithms, automated path generation
• Software engineering issues: data structure, data base, knowledge base, planning algorithms, user interface, software interface
Notes: <number>

## Slide 53: A FEATURE BASED DESIGN/ PROCESS PLANNING SYSTEM
Geometric Reasoning
Application-Specific Features (e.g. manufacturing features)
  blind slot, through slot, step, etc.
  approach direction, feed direction
  feature relations: precedence and intersection type
Manufacturing-Oriented Design Features
  hole, straight slot, T-slot, circular slot, pocket
  counterbore, sculptured surface cavity
Principle:
  Provide designer with the freedom to describe shape -
  avoid constraining manufacturing planning
  or requiring detailed manufacturing knowledge.
Notes: <number>

## Slide 54: SOME AUTOMATED PROCESS PLANNING EFFORTS
U. Mass, Dixon: Features-based design for manufacturing analysis of extrusions, castings, injection molding
ASU, Shah: Theory of features study for CAM-I; Feature-mapping shell
Stanford,Cutkosky: feature-based design, process planning, fixturing systems.
Helsinki, Mantyla: systems for design & process planning.
IBM, Rossignac:Editing & validation of feature models; MAMOUR system.
SDRC, Chung, GE, Simmons: Feature-based design and casting analysis.
NIST : Automated process planning
CAM-I, UTRC: XPS-2, generative process planning
U of Maryland, Nau: Semi-generative process planning
GE R & D, Hines: Art to Part
Penn State, Wysk (Texas A&M): graph based process planning
Stanford, Cutkosky: FirstCut, integrated design and manufacturing system based on features.
CMI & CMU: IMW, feature based design, expert operation planning.
U. of Twente, Holland, Kals: PARTS , feature based input, feature recognition, operation planning.
Allied Bendix, Hummel & Brooks: XCUT system for cavity operation planning.
IPK Berlin & IPK Aachen
UMIST, B.J. Davies
U. of Leeds, de Pennington
U. of Tokyo, Kimura
Features in Process Planning
Feature in Design
QTC is one of the only efforts that considers design through inspection and the only one that uses deep geometric reasoning to link design and process planning.
Notes: <number>

## Slide 55: SOME APPROACHES
Notes: <number>

## Slide 56: THE DEVELOPMENT OF CAPP
Notes: <number>