## Slide 1
PREPARATION OF HISTOLOGICAL SPECIMENS

## Slide 2: TISSUE FIXATION
Fixation is a complex series of chemical events that differ for the different groups of substance found in tissues.
The aim of fixation:
1- To prevent autolysis and bacterial attack.
2- To fix the tissues so they will not change their volume and shape during processing.
3- To prepare tissue and leave it in a condition which allow clear staining of sections.
4- To leave tissue as close as their living state as possible, and no small molecules should be lost.
Fixation is coming by reaction between the fixative and protein which form a gel, so keeping every thing as their in vivo relation to each other.

## Slide 3
Factors affect fixation:
- PH.
- Temperature.
- Penetration of fixative.
- Volume of tissue.
According to previous factors we can determine the concentration of fixative and fixation time.
Types of fixative:
Acetic acid, Formaldehyde, Ethanol, Glutaraldehyde, Methanol and Picric acid.

## Slide 4
TISSUE PROCESSING
the aim of tissue processing is to embed the tissue in a solid medium firm enough to support the tissue and give it sufficient rigidity to enable thin sections to be cut , and yet soft enough not to damage the knife or tissue.
Stages of processing:
1- Dehydration.
2- Clearing.
3- Embedding.

## Slide 5: Dehydration
to remove fixative and water from the tissue and replace them with dehydrating fluid.
There are a variety of compounds many of which are alcohols. several are hydrophilic so attract water from tissue.
To minimize tissue distortion from diffusion currents, delicate specimens are dehydrated in a graded ethanol series from water through 10%-20%-50%-95%-100% ethanol.
In the paraffin wax method, following any necessary post fixation treatment, dehydration from aqueous fixatives is usually initiated in 60%-70% ethanol, progressing through 90%-95% ethanol, then two or three changes of absolute ethanol before proceeding to the clearing stage.

## Slide 6
Types of dehydrating agents:
Ethanol, Methanol, Acetone.
Duration of dehydration should be kept to the minimum consistent with the tissues being processed. Tissue blocks 1 mm thick should receive up to 30 minutes in each alcohol, blocks 5 mm thick require up to 90 minutes or longer in each change. Tissues may be held and stored indefinitely in 70% ethanol without harm

## Slide 7: Clearing
replacing the dehydrating fluid with a fluid that is totally miscible with both the dehydrating fluid and the embedding medium.
Choice of a clearing agent depends upon the following:
- The type of tissues to be processed, and the type of processing to be undertaken.
- The processor system to be used.
- Intended processing conditions such as temperature, vacuum and pressure.
- Safety factors.
- Cost and convenience.
- Speedy removal of dehydrating agent .
- Ease of removal by molten paraffin wax .
- Minimal tissue damage .

## Slide 8
Some clearing agents:
- Zylene.
- Toluene.
- Chloroform.
- Benzene.
- Petrol.

## Slide 9: Embedding
is the process by which tissues are surrounded by a medium such as agar, gelatin, or wax which when solidified will provide sufficient external support during sectioning.
Paraffin wax properties :
Paraffin wax is a polycrystalline mixture of solid hydrocarbons produced during the refining of coal and mineral oils. It is about two thirds the density and slightly more elastic than dried protein. Paraffin wax is traditionally marketed by its melting points which range from 39°C to 68°C.
The properties of paraffin wax are improved for histological purposes by the inclusion of substances added alone or in combination to the wax:
- improve ribboning.
- increase hardness.
- decrease melting point
- improve adhesion between specimen and wax

## Slide 10: Precaution while embedding in wax
The wax is clear of clearing agent.
No dust particles must be present.
Immediately after tissue embedding, the wax must be rapidly cooled to reduce the wax crystal size.

## Slide 11
There are four main mould systems and associated embedding protocols presently in use :
1- traditional methods using paper boats
2- Leuckart or Dimmock embedding irons or metal containers
3- the Peel-a-way system using disposable plastic moulds and
4- systems using embedding rings or cassette-bases which become an integral part of the block and serve as the block holder in the microtome.

## Slide 12
Tissue processing Embedding moulds:
(A) paper boat;
(B) metal bot mould;
(C) Dimmock embedding mould;
(D) Peel-a-way disposable mould;
(E) base mould used with embedding ring ( F) or cassette bases (G)

## Slide 13
General Embedding Procedure 1- Open the tissue cassette, check against worksheet entry to ensure the correct number of tissue pieces are present.
2- Select the mould, there should be sufficient room for the tissue with allowance for at least a 2 mm surrounding margin of wax.
3- Fill the mould with paraffin wax.
4 Using warm forceps select the tissue, taking care that it does not cool in the air; at the same time.
5- Chill the mould on the cold plate, orienting the tissue and firming it into the wax with warmed forceps. This ensures that the correct orientation is maintained and the tissue surface to be sectioned is kept flat.
6- Insert the identifying label or place the labeled embedding ring or cassette base onto the mould.
7- Cool the block on the cold plate, or carefully submerge it under water when a thin skin has formed over the wax surface.
8- Remove the block from the mould.
9- Cross check block, label and worksheet.

## Slide 15
ORIENTATION OF TISSUE IN THE BLOCK Correct orientation of tissue in a mould is the most important step in embedding. Incorrect placement of tissues may result in diagnostically important tissue elements being missed or damaged during microtomy.
elongate tissues are placed diagonally across the block
tubular and walled specimens such as vas deferens, cysts and gastrointestinal tissues are embedded so as to provide transverse sections showing all tissue layers
tissues with an epithelial surface such as skin, are embedded to provide sections in a plane at right angles to the surface (hairy or keratinised epithelia are oriented to face the knife diagonally)
multiple tissue pieces are aligned across the long axis of the mould, and not placed at random

## Slide 16: Processing methods and routine schedules
Machine processing
manual processing

## Slide 17: CUTTING
using the microtome

## Slide 18
A microtome is a mechanical instrument used to cut biological specimens into very thin segments for microscopic examination. Most microtomes use a steel blade and are used to prepare sections of animal or plant tissues for histology. The most common applications of microtomes are

## Slide 19
1- Traditional histological technique:
tissues are hardened by replacing water with paraffin. The tissue is then cut in the microtome at thicknesses varying from 2 to 25 micrometers thick. From there the tissue can be mounted on a microscope slide, stained and examined using a light microscope

## Slide 20
2- Cryosection:
water-rich tissues are hardened by freezing and cut frozen; sections are stained and examined with a light microscope. This technique is much faster than traditional histology (5 minutes vs. 16 hours) and are used in operations to achieve a quick diagnosis. Cryosections can also be used in immunohistochemistry as freezing tissue does not alter or mask its chemical composition as much as preserving it with a fixative.

## Slide 21
3- Electron microscopy:
after embedding tissues in epoxy resin, a microtome equipped with a glass or diamond knife is used to cut very thin sections (typically 60 to 100 nanometers). Sections are stained and examined with a transmission electron microscope. This instrument is often called an ultramicrotome.
4- Botanical microtomy:
hard materials like wood, bone and leather require a sledge microtome. These microtomes have heavier blades and cannot cut as thin a regular microtomy.
Microtome blades are extremely sharp, and should be handled with great care. Safety precautions should be taken in order to avoid any contact with the cutting edge of the blade.

## Slide 22: Microtome knives
STEEL KNIVES
NON-CORROSIVE KNIVES FOR CRYOSTATS
DISPOSABLE BLADES
GLASS KNIVES
DIAMOND KNIVES

## Slide 23: STAINING

## Slide 24
H & E is a charge-based, general purpose stain. Hematoxylin stains acidic molecules shades of blue. Eosin stains basic materials shades of red, pink and orange. H & E stains are universally used for routine histological examination of tissue sections.
Hematoxylin and Eosin (H & E)

## Slide 25
Fixation
  Any well fixed tissue.
Staining Procedure
    1- Deparaffinize and hydrate to water
    2- If sections are Zenker-fixed, remove the mercuric chloride crystals with iodine and clear with sodium thiosulphate (hypo)
    3- Mayer's hematoxylin for 15 minutes
    4- Wash in running tap water for 20 minutes
    5- Counterstain with eosin from 15 seconds to 2 minutes depending on the age of the eosin, and the depth of the counterstain desired. For even staining results dip slides several times before allowing them to set in the eosin for the desired time
    6- Dehydrate in 95% and absolute alcohols, two changes of 2 minutes each or until excess eosin is removed. Check under microscope
    7- Clear in xylene, two changes of 2 minutes each
    8- Mount in Permount or Histoclad
Results
  Nuclei - blue - with some metachromasia Cytoplasm - various shades of pink-identifying different tissue components

## Slide 26: Staining machine